## Slide 1: Integrating Mobile IoT Devices into the Arrowhead Framework Using Web of Things
Chiara Bonsignori, Carlo Puliafito,
Antonio Virdis, Enzo Mingozzi, Giuseppe Iannaccone

## Slide 2: Outline
Integration of legacy IoT devices within the Arrowhead Framework (AHF) through WoT
Using WoT towards mobility/migration support
Performance evaluation
Conclusions and future work

## Slide 3: Integration of legacy IoT devices within the AHF through WoT
The Arrowhead Framework (AHF) is an open-source platform for IoT interoperability and is currently supported as a project of the Eclipse Foundation2
Developed across several EU projects. We specifically worked in the Arrowhead Tools EU project3
  Main Objective: provide tools, platforms, engineering processes towards industrial automation
  80+ Partners from 18 EU Countries
  3 Years (May 2019 – July 2022)
Legacy devices: Devices that do not natively talk the same language nor use the same protocols of AHF entities.
2 https://projects.eclipse.org/projects/iot.arrowhead
3 https://www.arrowhead.eu/arrowheadtools

## Slide 4: Integration of legacy IoT devices within the AHF3
ECG device4
Size: 6.5 cm x 3.4 cm
BOM cost: <10$
Battery life: five days
Sampling rate: 320 Hz
Transmission rate: 5 kbps
Smart plug5
Size: 7.7 cm x 5.7 cm (without external case)
BOM cost: <15$
Monitors: active and reactive power, voltage, and current.
Remotely turn it on or off
3Work carried out within the scope of the Arrowhead Tools EU project: https://www.arrowhead.eu/arrowheadtools
4E. Spanò, S. Di Pascoli, and G. Iannaccone, “Low-power wearable ECG monitoring system for multiple-patient remote monitoring,” IEEE Sensors Journal, vol. 16, no. 13, pp. 5452–5462, 2016.
5E. Spanò, L. Niccolini, S. D. Pascoli, and G. Iannaccone, “Lastmeter smart grid embedded in an Internet-of-Things platform,” IEEE Transactions on Smart Grid, vol. 6, no. 1, pp. 468–476, 2015.

## Slide 5: Web of Things (WoT) – Main Components
Web Thing
Abstracts a physical or virtual entity
Has a JSON Thing Description (TD) associated
Consumer
Fetches and processes TD
Instantiates a Consumed Thing
Exposer
Servient
A software environment that can expose and/or consume Web Things
Exposer
Advertises TD
Instantiates an Exposed Thing

## Slide 6: Thing Description
Interaction Affordances
The capabilities offered by the Thing
Properties: state of the Thing
Actions: functions provided to manipulate the state
Events: to asynchronously notify Consumers
Protocol Bindings
Mapping from Interaction Affordances to concrete messages of protocols (HTTP, CoAP, MQTT, ….)

## Slide 7: Integration architecture
AHF consumers in a local cloud can access legacy devices
This architecture opens up opportunities towards edge computing

## Slide 8: Mobility/migration of WoT servients in edge computing

## Slide 9: Using WoT towards mobility/migration support
State management
We consider stateful servients at the edge. How to handle the state?
Managing (i.e., save, transfer, and restore) the state at the application-level is not transparent to the application itself
We choose to host a servient inside a container and migrate it using container migration techniques, transparently to the application
Addressing
Mobility/migration typically causes IP addresses to change
It is possible to use auxiliary elements (e.g., DNS), which however introduce complexity and potential delays
Our mechanisms to recover connectivity:
Are designed as part of WoT itself
Involve only the two endpoints
Are transparent to the application logic

## Slide 10: Mobility/Migration Support – Servient Migratability Configuration
10

## Slide 11: Mobility/Migration Support - Exposer Migration
After migration:
URIs of Interaction Affordances unreachable
notifications still received by Consumer
11

## Slide 12: Mobility/Migration Support - Consumer Migration
After migration:
URIs of Interaction Affordances still reachable
notifications no more received by Consumer
12
Additional data structure is required

## Slide 13: Performance evaluation - Testbed configuration
13

## Slide 14: Execution time of the consume()and produce() methods
14
Exposer

## Slide 15: Unavailability time due to Exposer and Consumer migration
15

## Slide 16: Conclusions
Integration of legacy devices (ECG and smart plug) into the AHF through WoT
Using WoT to support mobility/migration of servients in edge computing scenarios
Performance evaluation has shown a negligible overhead of our solution to baseline WoT and to the unavailability time perceived by endpoints
Future Work
Investigate the orchestration of the migration of multiple WoT servients
16

## Slide 17
Thank you!
carlo.puliafito@ing.unipi.it