## Slide 1: W3C Web of Things Summary and Applications
Michael McCool
February 2022

## Slide 2: Outline
What is WoT?
  Applying and extending web standards for IoT
  Descriptive interoperability: Thing Descriptions
  Finding Thing Descriptions: Discovery
Use Cases and Applications
  Use Cases and Requirements
  Smart Buildings
  Smart Cities
Discussion
  Gaps and Future Work

## Slide 3: W3C Web of Things (WoT)
W3C Working Group goal: Adapting web technologies to IoT
Already published: Thing Description (TD) metadata format
  TD describes the available interactions (network API) of a Thing
New deliverables in progress, including Discovery
  How does a potential user obtain the TD for a Thing?
App
App
App
HTTP
MQTT
Modbus
WS
AMQP
OPC-UA
KNX
BACnet
ECHONET
JSON
XML
EXI
CBOR
OAUTH2
API Key
Bearer
TLV
App
App
App
{ properties, actions, events }
WoT API
WoT API
WoT API
HTTP
MQTT
Modbus
WS
AMQP
OPC-UA
KNX
BACnet
ECHONET
JSON
XML
EXI
CBOR
OAUTH2
API Key
Bearer
TLV

## Slide 4: Descriptive Interoperability: TDs
WoT Thing Description (TD)
{
"@context": [
"https://www.w3.org/2019/wot/td/v1",
{ "iot": "http://iotschema.org/" }
],
"id": "urn:dev:org:32473:1234567890",
"title": "MyLEDThing",
"description": "RGB LED torchiere",
"@type": ["Thing", "iot:Light"],
"securityDefinitions": ["default": {
"scheme": "bearer"
}],
"security": ["default"],
"properties": {
"brightness": {
"@type": ["iot:Brightness"],
"type": "integer",
"minimum": 0,
"maximum": 100,
"forms": [ ... ]
}
},
"actions": {
"fadeIn": {
...
Door = Thing
Handle = Affordance
What?
How?
Open
Pull
Turn
WoT Architecture
  Constraints
    "Things" must have a TD
    Must use URIs, IANA media types, etc.
  Thing Description Affordances
    Describes WHAT the possible choices are
    Describes HOW to interact with the Thing

## Slide 5: Usage Patterns Overview

## Slide 6: Orchestration
Node-RED/node-gen
node-wot/Scripting API
WoTHelpers.fetch( "coap://localhost:5683/counter" ).then( async (td) => {
// using await for serial execution (note 'async' in then() of fetch())
try {
let thing = await WoT.consume(td);
console.info( "=== TD ===" );
console.info(td);
console.info( "==========" );
// read property #1
let read1 = await thing.readProperty( "count" );
console.info( "count value is" , read1);
// increment property #1 (without step)
await thing.invokeAction( "increment" );
let inc1 = await thing.readProperty( "count" );
console.info( "count value after increment #1 is" , inc1);
// increment property #2 (with step)
await thing.invokeAction( "increment" , {'step' : 3});
let inc2 = await thing.readProperty( "count" );
console.info( "count value after increment #2 (with step 3) is" , inc2);
// decrement property
await thing.invokeAction( "decrement" );
let dec1 = await thing.readProperty( "count" );
console.info( "count value after decrement is" , dec1);
} catch(err) {
console.error( "Script error:" , err);
}
}).catch( (err) => { console.error( "Fetch error:" , err); });

## Slide 7: Discovery
Goal: Obtain TD of interest
  Not limited to local network
  Scalable to many TDs
  Need to preserve privacy
  Phased access:
    Introduction: open
    Exploration: controlled
  Searchable via JSON Path, XPath, or SPARQL
Future work:
  Find "nearby" Things using geospatial data
Phase 1: Introduction
Phase 2: Exploration

## Slide 8: Deliverables
New/Updated Normative Documents:
Architecture 1.1: https://github.com/w3c/wot-architecture
Thing Description 1.1: https://github.com/w3c/wot-thing-description
Discovery: https://github.com/w3c/wot-discovery
Profiles: https://github.com/w3c/wot-profile
New/Updated Informative Documents:
Binding Templates: https://github.com/w3c/wot-binding-templates
Scripting API: https://github.com/w3c/wot-scripting-api
Use Cases and Requirements: https://github.com/w3c/wot-usecases
Community Resources:
Web Site: https://www.w3.org/WoT/

## Slide 9: Recent Activity
Plugfests
  https://github.com/w3c/wot-testing/tree/main/events
New Commercial Usages
  Takenaka Construction – Smart Building Information Management systems
  Netzo – IoT dashboards and device management
Directory Implementations
  WoT Hive, LogiLab (SPARQL based), Fraunhofer LinkSmart
IETF Relationships: JSON Path, CoreRD, COSE/JOSE, ASDF
Under Discussion:
  Geospatial data, Embedded JSON Signatures
  New Charters/New Deliverables

## Slide 10: Use Cases and Requirements
Informative Deliverable: https://github.com/w3c/wot-usecases
Purpose and Process:
Identify specific use cases
Identify application domains
  Collect use cases from other W3C groups
  Collect use cases from other stakeholders and SDOs
Identify usage patterns
  For example, hubs, proxies, automation, etc.
Identify relevant technologies
  For example, edge computing, digital twins, etc.
 Extract common requirements to drive current and future work

## Slide 11: Use Cases / Requirements Process
Use Case TF (IG)
Spec creation (WG)
Use Case
Gaps
New Building Block
TD
Profile
Shortlist
Use Case
Use Case
Use Case
s
Requirement
Security
Discovery
Scripting
System Architecture / Configuration
WoT Deliverables

## Slide 12: WoT Use Cases Relevant to Smart Cities
Smart City
  Geolocation
  Dashboard
  Interactive Public Spaces
  Meeting/Event Assistance
  Smart Campus
  Cultural Spaces
Health
  Public Health Monitoring
Energy
  Smart GRids
Building Technologies
  Smart Building
  Connected Bldg Energy Efficiency
  Automated Smart Bldg Management
  Portable Bldg Applications
Retail
  All Stop Emergency Plunger
  Door Sensor
  Freezers and Refrigerators
  Restrooms
  Lighting
  Canopies
  Cameras

## Slide 13: Recent Relevant Applications
Takenaka Corporation
EQ House, Tokyo 2019
BIM applications
Siemens
Desigo CC BIM Viewer
Netzo
IoT Data Hub
Dashboards

## Slide 14: Gaps and Discussion
GIS Integration
  Geospatial data and discovery
Data Management
  Digital Twins and shadows
  Event notifications
  Data management
Security
  Key provisioning and onboarding
  Secure LAN access
  Proxy services
  Access control and ad-hoc sharing
  MUDS
Accessibility
  Sensory modality mapping
  Textual/descriptive interfaces
  Service location
  Mobility services
Advanced Use Cases
  Transportation
  Logistics
  Distributed energy management
  AR visualization
  Analytics integration e.g. for health and safety monitoring

## Slide 15: Resources and Contacts
Dr. Michael McCool
Principal Engineer
Intel
Technology Pathfinding
michael.mccool@intel.com
Dr. Sebastian Kaebisch
Senior Key Expert
Siemens
Technology
sebastian.kaebisch@siemens.com
https://www.w3.org/WoT