## Slide 1: W3C Web of Things Retail Demo Scenario
Michael McCool
3 May 2022
Conexxus Conference

## Slide 2: Outline
What is WoT?
  Applying and extending web standards for IoT
  Descriptive interoperability
Test Scenario: Cooler Monitor
  Hub architecture
  Desired behavior and devices
Implementations
  Options
  Home Assistant and Node-RED Prototypes
Discussion
  Semantic interoperability

## Slide 3: W3C Web of Things (WoT)
W3C Working Group goal: Adapting web technologies to IoT
Already published: Thing Description (TD) metadata format
  TD describes the available interactions (network API) of a Thing
New deliverables in progress, including Discovery
  How does a potential user obtain the TD for a Thing?
App
App
App
HTTP
MQTT
Modbus
WS
AMQP
OPC-UA
KNX
BACnet
ECHONET
JSON
XML
EXI
CBOR
OAUTH2
API Key
Bearer
TLV
App
App
App
{ properties, actions, events }
WoT API
WoT API
WoT API
HTTP
MQTT
Modbus
WS
AMQP
OPC-UA
KNX
BACnet
ECHONET
JSON
XML
EXI
CBOR
OAUTH2
API Key
Bearer
TLV

## Slide 4: Descriptive Interoperability: TDs
WoT Thing Description (TD)
{
"@context": [
"https://www.w3.org/2022/wot/td/v1.1",
{ "iot": "http://iotschema.org/" }
],
"id": "urn:dev:org:32473:1234567890",
"title": "MyLEDThing",
"description": "RGB LED torchiere",
"@type": ["Thing", "iot:Light"],
"securityDefinitions": {
"default": {"scheme": "bearer"}
},
"security": ["default"],
"properties": {
"brightness": {
"@type": ["iot:Brightness"],
"type": "integer",
"minimum": 0,
"maximum": 100,
"forms": [ ... ]
}
},
"actions": {
"fadeIn": {
...
Door = Thing
Handle = Affordance
What?
How?
Open
Pull
Turn
WoT Architecture
  Constraints
    "Things" must have a TD
    Must use URIs, IANA media types, etc.
  Thing Description Affordances
    Describes WHAT the possible choices are
    Describes HOW to interact with the Thing

## Slide 5: Usage Patterns Overview

## Slide 6: Discovery
Goal: Obtain TD of interest
  Not limited to local network
  Scalable to many TDs
  Need to preserve privacy
  Phased access:
    Introduction: open
    Exploration: controlled
  Searchable via JSON Path, XPath, or SPARQL
Future work:
  Find "nearby" Things using geospatial data
Phase 1: Introduction
Phase 2: Exploration

## Slide 7: Orchestration
Node-RED/node-gen
node-wot/Scripting API
WoTHelpers.fetch( "coap://localhost:5683/counter" ).then( async (td) => {
// using await for serial execution (note 'async' in then() of fetch())
try {
const thing = await WoT.consume(td);
console.info( "=== TD ===" );
console.info(td);
console.info( "==========" );
// read property #1
const read1 = await thing.readProperty( "count" );
console.info( "count value is" , await read1.value());
// increment property #1 (without step)
await thing.invokeAction( "increment" );
const inc1 = await thing.readProperty( "count" );
console.info( "count value after increment #1 is" , await inc1.value());
// increment property #2 (with step)
await thing.invokeAction( "increment" , {'step' : 3});
const inc2 = await thing.readProperty( "count" );
console.info( "count value after increment #2 (w/ step 3) is" , await inc2.value());
// decrement property
await thing.invokeAction( "decrement", undefined, {
formIndex: getFormIndexForDecrementWithCoAP(thing);
} );
const dec1 = await thing.readProperty( "count" );
console.info( "count value after decrement is" , await dec1.value());
} catch(err) {
console.error( "Script error:", err);
}
}).catch( (err) => { console.error( "Fetch error:", err); });

## Slide 8: Applications
https://www.takenaka.co.jp/news/2021/05/02/
Takenaka Corporation
CGLL Platform - BIM
https://new.siemens.com/global/en/products/buildings/automation/desigo.html
https://www.evosoft.com/en/digitalization-offering/saywot/
Siemens
Desigo CC – BIM
Say WoT!
https://netzo.io/
Netzo
IoT Data Hub
Dashboards
https://www.eclipse.org/ditto/2022-03-03-wot-integration.html
Bosch
Eclipse Ditto - Digital twin

## Slide 9: Test Scenario: Cooler Monitor
Multi-color Light
Temperature Gauge
Door Sensor
Rule Engine
TD
Cooler
Protocol Gateway
Other
HTTP
TD
TD
TD
TD
TD
Hub
Remote Access

## Slide 10: Why a Hub?
Protocol translation
Data translation
Other services
  Historical data
  Dashboards
Rules engine (automation)
Shadowing
  Caching state of sleeping devices
  Queuing commands to sleeping devices
  Important for battery-powered devices
Secure Remote Access

## Slide 11: Desired Behavior
Door Open Alert
If the cooler door has been left open for more than a certain time: flash light.
If the door is closed: cancel flashing
Temperature Out of Range
If internal freezer temp is too low: turn light BLUE
If internal freezer temp is too high: turn light RED
If internal freezer temp is normal: turn light WHITE
NOTE:
Rules should co-exist.
 If door is open and temps are high, light should be RED and flashing

## Slide 12: Devices
Test Devices
Commercial Devices

## Slide 13: Video: System Demo
https://youtu.be/m0F11Vu2wf8

## Slide 14: Implementation Approaches
Proprietary Turnkey System
  Contract out entire system to a third party
  Issues: Maintenance, modifications, ownership transfer, business risk
Proprietary Gateway/Rules Engine (e.g. Smart Things)
  Integrations limited to those provided by vendor, business risk, portability
Open-source Gateway/Rules Engine (e.g. Home Assistant, Node-RED)
  Crowdsourced integrations, variable quality, business risk, portability
Standards-based Gateway/Rules Engine (e.g. node-wot)
  Subclass of Proprietary and Open-Sourced Gateways
  Addresses portability concern, which also helps to address business risk

## Slide 15: Two Implementations
Home Assistant Native Rules
Use built-in rules engine
Node RED
Rules based on WoT TD/node-wot

## Slide 16: Home Assistant – Native Rule Engine
HA is used as a "typical" gateway
  EdgeX Foundry would be more appropriate for retail
Frontend provides an HTTP API
Backend supports a variety of device/ecosystem integrations
  Hue is HTTP (proxy to Zigbee)
  NCD Temp is MQTT
  Shelly is MQTT and HTTP
  Test RGBW strip, dial, button, and temp sensors are MQTT and HTTP, generated via ESPHome
Automation rules are based on HA-specific YAML configuration scripts

## Slide 17: Home Assistant – Dashboard

## Slide 18: Home Assistant – Rules

## Slide 19: Home Assistant – Temp High Rule

## Slide 20: Home Assistant – Temp High Rule

## Slide 21: Node-RED/WoT Discovery
Node-RED is an open-source rule engine
An extension can be used to discover WoT TDs and interface to what they describe
In the demo we use HA as a gateway
HOWEVER, we could also talk directly to devices via MQTT (for example), given a suitable WoT TD
Automation rules are based on Node-RED "flows"

## Slide 22: Node-RED – Temp Rule

## Slide 23: Node-RED Subflows

## Slide 24: Interoperability
WoT TDs describe device interfaces in a standard way
  Interactions are now is protocol and payload encoding independent
HOWEVER, devices that do the "same" thing may still have different data models and behavior...

## Slide 25: Semantic Interoperability
WoT Thing Descriptions
  Currently address "syntactic interoperability"
  Transform multiple protocols into a common interaction abstraction
  Transform multiple payload encodings into a common format (JSON)
Next Steps
  Annotating Thing Description with semantics
  Transform data into a standardized data model
  WoT TDs are encoded using JSON-RD, which provides for semantic annotation and inferencing
  Still need (Conexxus can contribute here):
    Use cases driving required operations and behavior
    Common semantic vocabularies
    Standardized data models

## Slide 26: Resources and Contacts
Dr. Michael McCool
Principal Engineer
Intel
Technology Pathfinding
michael.mccool@intel.com
Dr. Sebastian Kaebisch
Senior Key Expert
Siemens
Technology
sebastian.kaebisch@siemens.com
https://www.w3.org/WoT