## Slide 1: W3C Web of Things Summary and Status Update
Michael McCool
10 March 2022

## Slide 2: Outline
What is WoT?
  Applying and extending web standards for IoT
  Descriptive interoperability: Thing Descriptions
  Finding Thing Descriptions: Discovery
  Use Cases and Requirements
Recent Activity
  Testfest/Plugfest
  Applications
Discussion
  Gaps and Future Work

## Slide 3: W3C Web of Things (WoT)
W3C Working Group goal: Adapting web technologies to IoT
Already published: Thing Description (TD) metadata format
  TD describes the available interactions (network API) of a Thing
New deliverables in progress, including Discovery
  How does a potential user obtain the TD for a Thing?
App
App
App
HTTP
MQTT
Modbus
WS
AMQP
OPC-UA
KNX
BACnet
ECHONET
JSON
XML
EXI
CBOR
OAUTH2
API Key
Bearer
TLV
App
App
App
{ properties, actions, events }
WoT API
WoT API
WoT API
HTTP
MQTT
Modbus
WS
AMQP
OPC-UA
KNX
BACnet
ECHONET
JSON
XML
EXI
CBOR
OAUTH2
API Key
Bearer
TLV

## Slide 4: Descriptive Interoperability: TDs
WoT Thing Description (TD)
{
"@context": [
"https://www.w3.org/2022/wot/td/v1.1",
{ "iot": "http://iotschema.org/" }
],
"id": "urn:dev:org:32473:1234567890",
"title": "MyLEDThing",
"description": "RGB LED torchiere",
"@type": ["Thing", "iot:Light"],
"securityDefinitions": {
"default": {"scheme": "bearer"}
},
"security": ["default"],
"properties": {
"brightness": {
"@type": ["iot:Brightness"],
"type": "integer",
"minimum": 0,
"maximum": 100,
"forms": [ ... ]
}
},
"actions": {
"fadeIn": {
...
Door = Thing
Handle = Affordance
What?
How?
Open
Pull
Turn
WoT Architecture
  Constraints
    "Things" must have a TD
    Must use URIs, IANA media types, etc.
  Thing Description Affordances
    Describes WHAT the possible choices are
    Describes HOW to interact with the Thing

## Slide 5: Usage Patterns Overview

## Slide 6: Discovery
Goal: Obtain TD of interest
  Not limited to local network
  Scalable to many TDs
  Need to preserve privacy
  Phased access:
    Introduction: open
    Exploration: controlled
  Searchable via JSON Path, XPath, or SPARQL
Future work:
  Find "nearby" Things using geospatial data

## Slide 7: Orchestration
Node-RED/node-gen
node-wot/Scripting API
WoTHelpers.fetch( "coap://localhost:5683/counter" ).then( async (td) => {
// using await for serial execution (note 'async' in then() of fetch())
try {
const thing = await WoT.consume(td);
console.info( "=== TD ===" );
console.info(td);
console.info( "==========" );
// read property #1
const read1 = await thing.readProperty( "count" );
console.info( "count value is" , await read1.value());
// increment property #1 (without step)
await thing.invokeAction( "increment" );
const inc1 = await thing.readProperty( "count" );
console.info( "count value after increment #1 is" , await inc1.value());
// increment property #2 (with step)
await thing.invokeAction( "increment" , {'step' : 3});
const inc2 = await thing.readProperty( "count" );
console.info( "count value after increment #2 (w/ step 3) is" , await inc2.value());
// decrement property
await thing.invokeAction( "decrement", undefined, {
formIndex: getFormIndexForDecrementWithCoAP(thing);
} );
const dec1 = await thing.readProperty( "count" );
console.info( "count value after decrement is" , await dec1.value());
} catch(err) {
console.error( "Script error:", err);
}
}).catch( (err) => { console.error( "Fetch error:", err); });

## Slide 8: Use Cases and Requirements
Informative Deliverable: https://github.com/w3c/wot-usecases
Purpose and Process:
Identify specific use cases
Identify application domains
  Collect use cases from other W3C groups
  Collect use cases from other stakeholders and SDOs
Identify usage patterns
  For example, hubs, proxies, automation, etc.
Identify relevant technologies
  For example, edge computing, digital twins, etc.
 Extract common requirements to drive current and future work

## Slide 9: Use Cases / Requirements Process
Use Case TF (IG)
Spec creation (WG)
Use Case
Gaps
New Building Block
TD
Profile
Shortlist
Use Case
Use Case
Use Case
s
Requirement
Security
Discovery
Scripting
System Architecture / Configuration
WoT Deliverables

## Slide 10: Deliverables
New/Updated Normative Documents:
Architecture 1.1: https://github.com/w3c/wot-architecture
Thing Description 1.1: https://github.com/w3c/wot-thing-description
Discovery: https://github.com/w3c/wot-discovery
Profiles: https://github.com/w3c/wot-profile
New/Updated Informative Documents:
Binding Templates: https://github.com/w3c/wot-binding-templates
Scripting API: https://github.com/w3c/wot-scripting-api
Use Cases and Requirements: https://github.com/w3c/wot-usecases
Community Resources:
Web Site: https://www.w3.org/WoT/

## Slide 11: Recent Activity
Plugfest/Testfest: Aug 29-Sept 2
  https://github.com/w3c/wot-testing/tree/main/events
New Commercial Usages
  Takenaka Construction – Smart Building Information Management systems
  Netzo – IoT dashboards and device management
Directory Implementations
  WoT Hive, LogiLab (SPARQL based), Fraunhofer LinkSmart, TinyIoT
IETF Relationships: JSON Path, CoreRD, COSE/JOSE, ASDF
Under Discussion:
  New Charters/New Deliverables/Updates to existing specifications
  Geolocation, Onboarding, Historical data: proposals/deliverable-proposals

## Slide 12: Applications
https://www.takenaka.co.jp/news/2021/05/02/
Takenaka Corporation
CGLL Platform - BIM
https://new.siemens.com/global/en/products/buildings/automation/desigo.html
https://www.evosoft.com/en/digitalization-offering/saywot/
Siemens
Desigo CC – BIM
Say WoT!
https://netzo.io/
Netzo
IoT Data Hub
Dashboards
https://www.eclipse.org/ditto/2022-03-03-wot-integration.html
Bosch
Eclipse Ditto - Digital twin

## Slide 13: Discussion: Some Possible Next Steps
GIS Integration
  Geospatial data and discovery
Data Management
  Digital Twins and shadows
  Event notifications
  Data management
Security
  Key provisioning and onboarding
  Secure LAN access
  Proxy services
  Access control and ad-hoc sharing
  MUDS
Accessibility
  Sensory modality mapping
  Textual/descriptive interfaces
  Service location
  Mobility services
Advanced Use Cases
  Transportation
  Logistics
  Distributed energy management
  AR visualization
  Analytics integration e.g. for health and safety monitoring

## Slide 14: Resources and Contacts
Dr. Michael McCool
Principal Engineer
Intel
Technology Pathfinding
michael.mccool@intel.com
Dr. Sebastian Kaebisch
Senior Key Expert
Siemens
Technology
sebastian.kaebisch@siemens.com
https://www.w3.org/WoT