## Slide 1: W3C Web of Things Status and Spatial Discovery
Michael McCool
26 October 2022
Presented to Metaverse Real/Virtual World Integration WG

## Slide 2: Outline
What is WoT?
  Applying and extending web standards for IoT
  Descriptive interoperability: Thing Descriptions
  Applications and implementations
  Finding Thing Descriptions: Discovery
Spatial Localization
  Dynamic vs. static locations
  Geolocation extensions for Discovery
  Interval queries
Next Steps

## Slide 3: W3C Web of Things (WoT)
W3C Working Group goal: Adapting web technologies to IoT
Already published: Thing Description (TD) JSON-LD metadata format
  TD describes the available interactions (network API) of a Thing
New deliverables in progress, including Discovery
  How does a potential user obtain the TD for a Thing?
App
App
App
HTTP
MQTT
Modbus
WS
AMQP
OPC-UA
KNX
BACnet
ECHONET
JSON
XML
EXI
CBOR
OAUTH2
API Key
Bearer
TLV
App
App
App
{ properties, actions, events }
WoT API
WoT API
WoT API
HTTP
MQTT
Modbus
WS
AMQP
OPC-UA
KNX
BACnet
ECHONET
JSON
XML
EXI
CBOR
OAUTH2
API Key
Bearer
TLV

## Slide 4: Descriptive Interoperability: TDs
WoT Thing Description (TD)
{
"@context": [
"https://www.w3.org/2022/wot/td/v1.1",
{ "iot": "http://iotschema.org/" }
],
"id": "urn:dev:org:32473:1234567890",
"title": "MyLEDThing",
"description": "RGB LED torchiere",
"@type": ["Thing", "iot:Light"],
"securityDefinitions": {
"default": {"scheme": "bearer"}
},
"security": ["default"],
"properties": {
"brightness": {
"@type": ["iot:Brightness"],
"type": "integer",
"minimum": 0,
"maximum": 100,
"forms": [ ... ]
}
},
"actions": {
"fadeIn": {
...
Door = Thing
Handle = Affordance
What?
How?
Open
Pull
Turn
WoT Architecture
  Constraints
    "Things" must have a TD
    Must use URIs, IANA media types, etc.
  Thing Description Affordances
    Describes WHAT the possible choices are
    Describes HOW to interact with the Thing

## Slide 5: Usage Patterns Overview

## Slide 6: Orchestration
Node-RED/node-gen
node-wot/Scripting API
WoTHelpers.fetch( "coap://localhost:5683/counter" ).then( async (td) => {
// using await for serial execution (note 'async' in then() of fetch())
try {
const thing = await WoT.consume(td);
console.info( "=== TD ===" );
console.info(td);
console.info( "==========" );
// read property #1
const read1 = await thing.readProperty( "count" );
console.info( "count value is" , await read1.value());
// increment property #1 (without step)
await thing.invokeAction( "increment" );
const inc1 = await thing.readProperty( "count" );
console.info( "count value after increment #1 is" , await inc1.value());
// increment property #2 (with step)
await thing.invokeAction( "increment" , {'step' : 3});
const inc2 = await thing.readProperty( "count" );
console.info( "count value after increment #2 (w/ step 3) is" , await inc2.value());
// decrement property
await thing.invokeAction( "decrement", undefined, {
formIndex: getFormIndexForDecrementWithCoAP(thing);
} );
const dec1 = await thing.readProperty( "count" );
console.info( "count value after decrement is" , await dec1.value());
} catch(err) {
console.error( "Script error:", err);
}
}).catch( (err) => { console.error( "Fetch error:", err); });

## Slide 7: Use Cases and Requirements
Informative Deliverable: https://github.com/w3c/wot-usecases
Purpose and Process:
Identify specific use cases
Identify application domains
  Collect use cases from other W3C groups
  Collect use cases from other stakeholders and SDOs
Identify usage patterns
  For example, hubs, proxies, automation, etc.
Identify relevant technologies
  For example, edge computing, digital twins, etc.
 Extract common requirements to drive current and future work

## Slide 8: Use Cases / Requirements Process
Use Case TF (IG)
Spec creation (WG)
Use Case
Gaps
New Building Block
TD
Profile
Shortlist
Use Case
Use Case
Use Case
s
Requirement
Security
Discovery
Scripting
System Architecture / Configuration
WoT Deliverables

## Slide 9: Deliverables
New/Updated Normative Documents:
Architecture 1.1: https://github.com/w3c/wot-architecture
Thing Description 1.1: https://github.com/w3c/wot-thing-description
Discovery: https://github.com/w3c/wot-discovery
New/Updated Informative Documents:
Binding Templates: https://github.com/w3c/wot-binding-templates
Scripting API: https://github.com/w3c/wot-scripting-api
Use Cases and Requirements: https://github.com/w3c/wot-usecases
Community Resources:
Web Site: https://www.w3.org/WoT/

## Slide 10: Recent Activity
Commercial Usages related to spatial localization and digital twins
  Takenaka Construction – Smart Building Information Management systems
  Siemens – Desigo CC Building Information Management systems
  Bosch – Ditto digital twins
  Netzo – IoT dashboards and device management
Directory Implementations
  WoT Hive
  LogiLab (SPARQL based)
  Fraunhofer LinkSmart
  VAIMEE

## Slide 11: Applications
https://www.takenaka.co.jp/news/2021/05/02/
Takenaka Corporation
CGLL Platform - BIM
https://new.siemens.com/global/en/products/buildings/automation/desigo.html
https://www.evosoft.com/en/digitalization-offering/saywot/
Siemens
Desigo CC – BIM
Say WoT!
https://netzo.io/
Netzo
IoT Data Hub
Dashboards
https://www.eclipse.org/ditto/2022-03-03-wot-integration.html
Bosch
Eclipse Ditto - Digital twin

## Slide 12: Discovery
Goal:
Obtain TD of interest
Not limited to local network
Scalable to many TDs
Need to preserve privacy
Architecture:
Phased access:
  Introduction: open
  Exploration: controlled access
Introduction mechanisms
  Direct, WK, DNS-SD, CoRE-RD, DID
Exploration mechanisms
  TD Server, Self, Directory
Directories searchable via
  JSON Path (IETF RFC pending)
  XPath 3.1
  SPARQL

## Slide 13: Discovery

## Slide 14: Discovery
Possible future work:
  Encode static geospatial data in Thing Descriptions
  Provide ontologies for dynamic geospatial data
  Index Things by location in TD Directories
  Provide geolocation filters in Introduction mechanisms
    e.g. geolocation filters in DNS-SD
  Discover Things using geospatial queries
    "find all Things within 100m of latitude 49.2803175 and longitude -123.1286623"
    "find all HVAC sensors in Room 101 of Sheraton Wall Vancouver"
  Both "quantitative" and "qualitative" locations important
  Also store sensor data and search based on interval queries
See:
  Geolocation proposal and examples
  Discussion for new WoT WG 2023 charter

## Slide 15: Example TDs using Geolocation
Simple static installation, using schema.org
Static installation, using modular (proposed) geolocation ontology
Dynamic installation, using internal geolocation resource
Dynamic installation, using separate geolocation service
Dynamic installation, geolocation service
Discovery extensions:
Spatially-aware introduction mechanisms (e.g. ext. DNS-SD or DID)
Query mechanisms for Directories (GeoSPARQL and/or JSONPath ext.)

## Slide 16: Gaps and Future Work
GIS Integration
  Geospatial data and discovery
Data Management
  Digital twins and shadows
  Event notifications
  Historical data
Security
  Key provisioning and onboarding
  Secure LAN access
  Proxy services
  Access control and ad-hoc sharing
  MUDS
Accessibility
  Sensory modality mapping
  Textual/descriptive interfaces
  Service location
  Mobility services
Advanced Use Cases
  Transportation
  Logistics
  Distributed energy management
  AR visualization
  Analytics integration e.g. for health and safety monitoring

## Slide 17: Resources and Contacts
Dr. Michael McCool
Principal Engineer
Intel
Technology Pathfinding
michael.mccool@intel.com
Dr. Sebastian Kaebisch
Senior Key Expert
Siemens
Technology
sebastian.kaebisch@siemens.com
https://www.w3.org/WoT