## Slide 1: Schema.org Extensions for IoT (iotschema)
2nd W3C Web of Things Workshop
Michael Koster, Darko Anicic, Aparna Thuluva

## Slide 2: What is iotschema ?
An open, publicly available, repository of semantic definitions for connected things
An extension of schema.org to enable descriptions of things in the physical world and their data
A community process for contribution and publication of standardized definitions
A way for domain experts to easily create semantic definitions that are relevant to their application domain

## Slide 3: What is iotschema (2)
A layer to bridge between device ecosystems and Semantic Web technologies
Normalize the device definitions from OCF, oneM2M etc.
Reuses property and relation types from existing ontologies and definitions
  SSN, SOSA, SAREF, QUDT
  Property types for e.g. Feature of Interest, units of measurement
Annotation vocabulary for WoT Thing Description
  Common definitions for application-specific Events, Actions, and Properties

## Slide 4: Diverse Devices and Applications, Common Protocols and Semantics
Transport
UDP/TCP
Protocols, Formats
IETF CoAP, CBOR, Link-Format
Device Ecosystems
OCF, OMA, Zigbee, Fairhair
Networks
WiFi, IPV6, Bluetooth
Protocol Binding
Thing Description
Semantic Vocab
W3C Thing Description
iotschema
Internet of Things
Narrow Waist
of Protocols
Web of Things
Narrow Waist
of Semantics
Applications
Interoperable Applications
Diverse Applications
Diverse Devices

## Slide 5: Who is iotschema for? For Different IoT Actors
Device vendors will use iotschema to publish protocol-neutral definitions of their devices to enable web scale adoption
IoT platform providers will use iotschema to make it easy for third party applications to use the platform
Application providers will use iotschema to make their applications portable across platforms
Domain experts will use iotschema to create domain-specific languages for connected things and their applications

## Slide 6
Semantic definitions that follow the design patterns and interaction affordances of connected things
Define a "Capability" that represents – typically – the smallest practical compose-able unit of functionality
For example, a temperature sensor, or a door lock
iotschema Semantic Definitions

## Slide 7: iotschema Semantic Definitions
iotschema semantic definitions consist of three categories, or classes, that describe a measurement or actuation, of some physical property or item
  A Capability describes measurement and actuation of some physical variable or set of variables, for example the temperature of something, or the brightness of a light bulb. A Capability has some related Interactions.
  An Interaction (Event, Action, or Property) describes an affordance to the capability, which may be to read or write a value, or perform a complex action.
  Data Item descriptions contain data types, units, minimum and maximum values, and other information about the data model, for example a shape or schema

## Slide 8: iotschema Model
schema:thing
Capability
InteractionPattern
Action
Event
Property
acceptsInputData
providesOutputData
providesInteractionPattern
rdfs:subclassOf
schema:Property
iotschema Class
Reused Class
DataItem
schema:PropertyValue
schema:PropertyValueSpec.

## Slide 9: Feature Of Interest Pattern
iotschema defines relationships between Capabilities and Features of Interest to describe connected physical systems

## Slide 10: iotschema Conceptual Integration with other ontologies
SSN, SOSA, SAREF concepts can extend a definition
Feature of Interest concepts and property types to describe location, equipment, or other classifiers
  For example: BrickSchema definitions from Haystack
Quantity and Units constraints can use QUDT concepts and appropriate identifiers

## Slide 11: Connect things to the real world
Door Lock
Door
DoorLock Capability
- ActuateLock Interaction
- ActuateUnlock Interaction
- GetState Interaction -> LockState Data
isAssociatedWith
- Is A Front Door
- Opens To Outside
- Is A Security Door
"Lock Security Doors and Check"
iotschema.org
other ontologies

## Slide 12: How is iotschema used?
Annotation of Thing Descriptions (W3C Web of Things)
A Thing Description represents a thing that can be annotated with iotschema capability terms
Thing Descriptions have Action, Event, and Property Interaction definitions that can be annotated with iotschema Interaction class terms
Thing Descriptions have DataSchema elements that can be annotated with iotschema Data Item class terms and constraints, such as data type, units
Thing Description enables applications to interact with connected things independent of protocol and platform

## Slide 13: How is iotschema used?
Interaction Pattern
Data Schema
Capability

## Slide 14: Thing Description Example
{ "@context": [ {"iot": http://iotschema.org/ } ],
"@type": ["Thing", "iot:TemperatureSensing"],
"name": "TemperatureSensor",
"iot:isAssociatedWith" : {"@id": "31.636", "@type": "iot:Room"},
“properties": {
“currentTemperature” : {
"@type": ["iot:Temperature"],
"isPropertyOf": {"@id": "31.636", "@type": "iot:Room"},
“properties": { "type":"number",
“schema:minValue": 0, “schema:maxValue” : 50,
“schema:unitCode”:”iot:Celsius” },
….
} ] }

## Slide 15: iotschema Node-RED

## Slide 16: iotschema Node-RED

## Slide 17: Status
Monthly Teleconferences since mid-2017
Examples of Definitions in a Github repository
FoI annotation examples are also in the repo
Prototypes tested at W3C Web of Things Plugfests and WISHI/IETF Hackathons from mid 2017
Contributors are ready to begin submitting definitions
Next steps are to build out tools and processes
W3C Community Group

## Slide 18: References
iotschema links
  https://github.com/iot-schema-collab/teleconferences/blob/master/README.md
  https://github.com/iot-schema-collab/intro-materials
  https://github.com/iot-schema-collab/teleconferences
iotschema Node-RED project
  https://github.com/iot-schema-collab/iotschema-node-red
W3C Community Group
  https://www.w3.org/community/iotschema/
  Provides an IPR framework for contribution

## Slide 19: Thank you

## Slide 20: Narrow Waist in System Design
OCF
dotdot
LWM2M
Fairhair
IP Networks LAN/WAN (WiFi, Thread)
Semantic Interoperability (Software Adaptation)
App
App
App
App
Many Applications. Local and Remote
Many Devices, Different Ecosystems
Common Infrastructure
(Protocols, Formats, and Meta Models)
Internet of Things
Web of Things

## Slide 21: Feature of Interest Integration
Features Of Interest (FoI) describe the real-world targets of sensing and actuation
Definitions may be developed in iot.schema.org, or more likely will come from domain experts
  GENIVI/VSS is a Specification for Automotive Features of Interest, called Branches, and actuation/measurement points, called Attributes and Signals
  BrickSchema is an adaptation of Haystack that defines Features of Interest of buildings and actuation or measurement points
iotschema defines relationships between Capabilities and Features of Interest to describe connected physical systems