## Slide 1: W3C WoT – Plugfest Nov 2024
Thread-connected KNX IoT devices
  Thread Border Router (Ethernet to Thread (wireless)
  Room unit (user interface to choose setpoint etc.)
  Sensors (room temperature, relative humidity, CO2)
  Valve actuator (PID controller + motor controls)
Main findings
  Sleepy devices: W3C WoT curently has no support
    Periodic wake-up, announced via mDNS (via TBR)
    Also common for Matter devices
  Security Schemes: OSCORE and SPAKE2+
    OSCORE scheme missing (any collaborators?)
    Combinations with different security bootstrapping mechanisms
  Discovery
    mDNS over IPv6 requires a lot of configuration on host OS
Ethernet + IPv6
IEEE 802.15.4
+ 6LoWPAN
+ Thread MLE
CoAP
(+ OSCORE
+ SPAKE2+)